## Slide 1
District of Columbia Water and Sewer Authority
George S. Hawkins, General Manager
June 20, 2011
Briefing on:
DC CLEAN RIVERS PROJECT
Anacostia River Projects
Division E – M Street Diversion Sewer
(CSOs 015, 016 and 017)
Briefing for:
CAPITAL RIVERFRONT BUSINESS IMPROVEMENT DISTRICT

## Slide 2: Agenda
What is a CSO?
Overview of CSO Program
DC Clean Rivers Project Snapshot
M Street Diversion Sewer (CSOs 015, 016 and 017)

## Slide 3: Combined Sewer Area
1/3 area is combined (12,478 acres)
53 CSO outfalls
  15 to Anacostia
  10 to Potomac
  28 to Rock Creek
Three receiving waters
  Anacostia River
  Potomac River
  Rock Creek

## Slide 4: What is a CSO?
100% of Suburbs
67% of DC
0% of suburbs
33% of DC

## Slide 5: Why are CSOs a Concern?
Can adversely affect quality of receiving waters
Primary concerns:
  Bacteria levels
  Contribute to low dissolved oxygen in water
    Potential for fish stress or fish kills
    Affects other aquatic life
  Aesthetics – contributes to trash on waterways
CSO 017 discharging to the Anacostia River during Hurricane Floyd

## Slide 6
Anacostia River
Interstate 395
Pennsylvania Avenue
Congressional Cemetery
Nationals
Stadium
Interstate 295
Sousa Brg
11th St Brg
S Capitol St Brg
Overview of CSO Program Anacostia River CSOs

## Slide 7: Project Snapshot
Anacostia River
Projects
Potomac & Rock Creek Projects
Storage & Conveyance Tunnel System
Most severely impacted by CSOs
Storage Tunnels
2025
2018
NORTH OF RFK
SOUTH OF RFK
2025
ENTIRE SYSTEM IN OPERATION

## Slide 8: Project Snapshot
Long Term Control Plan (LTCP)
  Control combined sewer overflows (CSOs)
  Reduce flooding
  Meet nutrient discharge limits of Chesapeake Bay Program
Schedule
  LTCP = 20 years (2005-2025)
  Nitrogen = 2007-2015
Cost
  LTCP = $2.5 billion
  Nitrogen = $950 M
  Total > $3.5 billion
Drivers
  Projects required to meet regulatory requirements (NPDES Permit and Consent Decrees)
A Blue Plains Tunnel
C CSO 019 Overflow and Diversion Structures
D JBAB Overflow and Potomac Outfall Sewer Diversion
E M Street Diversion Sewer (CSOs 015, 016 and 017)
G CSO 007 Diversion Structure and Diversion Sewer
H Anacostia River Tunnel
I Main Pumping Station and Tingey Street Diversions
J Northeast Boundary Tunnel
K Northeast Boundary Branch Tunnels
L Northeast Boundary Diversions
M Mt. Olivet Road Diversions
Y Blue Plains Dewatering Pumping Station and ECF
Z Poplar Point Pumping Station Replacement

## Slide 9: Other Clean Rivers Projects in the area

## Slide 10: M Street Diversion Sewer Purpose
Intercept CSO 015, 016 and 017 and convey flows to Anacostia River Tunnel (ART)
CSOs to be “consolidated”
  Divert full capacity of drainage area and convey to tunnel
  Removable bulkhead on outfall to river at diversion structure
  Remove bulkhead if maintenance of tunnel or appurtenances needed
CSO 017 Outfall @ Anacostia River

## Slide 11: M Street Diversion Sewer Project Location
River
CSO
015
CSO
016
CSO
017
Potomac River
Anacostia
Project Site

## Slide 12: M Street Diversion Sewer Existing Sewer System – CSOs 015, 016 and 017
12

## Slide 13: M Street Diversion Sewer Alignment
N

## Slide 14: M Street Diversion Sewer Construction Methods
Diversion sewer construction using trenchless technology
  Techniques for utility line installation, replacement, rehabilitation, inspection, location, and leak detection, with minimal excavation from the ground surface
  Less surface disruption
  Reduces environmental impacts
  Limits impacts to existing structures and utilities
  Reduce need for dewatering
  Reduce amount of excavated material
  Diversion Sewer length = 2,632-ft
  Diversion Sewer depth = 20 to 45-ft
  Construction of diversion chambers requires open-cut at three sites along alignment:
  9th and M Streets SE
  12th and M Street SE
  14th Street ROW and M Street SE

## Slide 15
Estimated Construction: October 2012 – February 2013
CSO 015
Construction Staging Area
U.S. Reservation 251
Key Plan

## Slide 16: M Street Diversion Sewer MOT for Structure 19 (AM Rush Hour)
Maintain 4 lanes of traffic – 3 westbound, 1 eastbound (AM)
Maintain South Sidewalk / protect Historic Wall
Reduced South Construction Zone (Navy Residences)
Relocate Bus Stop
9 TH ST. SE
8 TH ST. SE
7 TH ST. SE
M STREET SE
POTOMAC AVE. SE
REMOVE BUS STOP
STAGING AREA
DEMOLISH MEDIAN
DEMOLISH MEDIAN
CONSTRUCTION ZONE
9TH STREET GATE
RESUME NORMAL TRAFFIC PATTERN
RESUME NORMAL TRAFFIC PATTERN
RELOCATE BUS STOP
NEW BUS STOP
10 TH ST. SE
M STREET SE
Estimated Construction Period:
Dec 2012 to Feb 2013

## Slide 17: M Street Diversion Sewer MOT for Structure 19A (AM Rush Hour)
Maintain 4 lanes of traffic – 3 westbound, 1 eastbound (AM)
Maintain South Sidewalk / protect Historic Wall
Relocate Bus Stop
Right Turn out of 9th Street Gate only
9 TH ST. SE
8 TH ST. SE
7 TH ST. SE
M STREET SE
POTOMAC AVE. SE
REMOVE BUS STOP
STAGING AREA
REMOVE SIDEWALK
DEMOLISH MEDIAN
DEMOLISH MEDIAN
CONSTRUCTION ZONE
9TH STREET GATE
RESUME NORMAL TRAFFIC PATTERN
RESUME NORMAL TRAFFIC PATTERN
RELOCATE BUS STOP
NEW BUS STOP
10 TH ST. SE
M STREET SE
Estimated Construction Period:
Oct 2012 to Dec 2012

## Slide 18
CSO 016
Construction Staging Area
Estimated Construction: April 2012 – December 2013
U.S. Reservation 128
Key Plan

## Slide 19
CSO 017
Construction Staging Area
Estimated Construction: April 2012 – August 2013
U.S. Reservation 343-D
Anacostia River
Key Plan

## Slide 20: M Street Diversion Sewer Coordination with DDOT’s 11th Street Bridge Project
DDOT and DC Water are working together to reduce impacts on public/private landowners
Coordination Efforts
  Preliminary design coordination
  Monthly coordination meetings during Final Design – current phase
  Schedule coordination
  Sharing of design files
Preliminary Design Review Meeting Process
Maintenance of Traffic and Traffic Study Guidance
  Maintain 4 lanes of traffic at the intersection of 9th and M Streets SE

## Slide 21: M Street Diversion Sewer Schedule
Anacostia River Projects | CY 2010 |  |  |  | CY 2011 |  |  |  | CY 2012 |  |  |  | CY 2013 |  |  |  | CY 2014 |  |  |  | CY 2015 |  |  | 
 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
M Street Diversion Sewer |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Procurement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design – October 2010 through October 2011
Construction – April 2012 through December 2013
Current Status = 95% Design

## Slide 22: Next Steps
Complete Final Design
Bid/Award Construction – November/December 2011
Continue Public Outreach Program